## Slide 1
Ensemble-Variational Inversion System for Estimating Ammonia Emissions using CrIS Ammonia Retrievals
Michael Sitwell, Mark W. Shephard, and Yves Rochon
Air Quality Research Division, Environment and Climate Change Canada, Toronto, Ontario, Canada
Atmospheric Ammonia
  Primary atmospheric basic gas, important for particulate matter formation
  Short atmospheric lifetime (hours to days)
  Significant agricultural emissions (fertilizers and livestock)
Estimating ammonia emissions
  NH3 field is spatially very inhomogeneous
  In situ measurements can be challenging
  Satellite observations relatively new
  Large uncertainties on emissions
CrIS ammonia retrievals
  Ammonia retrievals available from instruments aboard S-NPP (2012-2021) and NOAA-20 (2019-present)
  Local overpass times at approximately 01:30 and 13:30
Goal: Refine NH3 emissions needed for the GEM-MACH air quality model
  Perform inversions for monthly mean ammonia emissions
  Use pre-existing time profiles to map monthly emissions to hourly emissions for use in GEM-MACH
Ensemble-based variational inversion system
  Flow-dependent background error covariance
  Does not require the model adjoint
  100 member ensemble with perturbed monthly mean NH3 emissions
Inversion Results
Impact on Particulate Matter Formation
Conclusions
Ammonia Emissions
Ensemble-Variational Inversion
While large uncertainties exist in NH3 emission inventories, emission inversions with CrIS NH3 retrievals can greatly reduce these uncertainties
Ensemble-based inversions are an effective method that does not require a model adjoint
Inversions yield better agreement with surface observations
NH3 inversions can have a significant impact on PM formation
Ensembles can be computationally expensive to run
9th International Symposium on Data Assimilation - October 16-20, 2023 - Bologna, Italy
Published in Sitwell, Michael, et al. "An ensemble-variational inversion system for the estimation of ammonia emissions using CrIS satellite ammonia retrievals." Atmospheric Chemistry and Physics 22.10 (2022): 6595-6624.
CrIS retrievals
emissions increment
inversion
NH3 emissions inventory
CrIS - GEM-MACH
NH3 total column
emissions-concentration background covariances
emissions 1
emissions 2
emissions 3
GEM-MACH
emissions ensemble
GEM-MACH
Monthly mean ammonia emission inversions for May to August 2016
  The inversion increases NH3 emissions in most of the model domain
Chart: Canada
| May | June | July | August
inventory | 140.7 | 48.4 | 41.1 | 45.1
inversion | 179.6 | 76.9 | 67.7 | 73.1
Chart: Contiguous US
| May | June | July | August
inventory | 315.9 | 456.6 | 426 | 335.3
inversion | 460.5 | 477.6 | 461.9 | 392.7
Changes in surface ammonia
  Inversions reduce underprediction of modeled surface NH3 as compared to surface observations
May
June
July
August
NH3 emissions increments
+ 28%
+ 59%
+ 65%
+ 62%
May
June
July
August
+ 46%
+ 5%
+ 8%
+ 17%
updated - original
mean bias (%)
mean bias (%)
ppbv
8
0
-8
Comparison with observations
  Some reduction in ammonium/nitrate underprediction as compared to surface/precipitation observations
Change in total ammonium/nitrate surface concentrations
CAPMoN
CASTNET
mean bias (%)
mean bias (%)
change over model domain
total surface ammonium + nitrate
change over model domain
change over model domain